## Slide 1
ACQUISITION · RESOLUTION · NOISE · DISTORTION
Visual Integrity: Investigating the Factors Shaping Image Quality
A Structured Analysis of the Factors That Shape Every Pixel
01
NAME:N.AKSHAYA
REG.NO:192425129
COURSE CODE:ITA0509
COURSE NAME:COMPUTER VISION
FACULTY:Yuvaraj S

## Slide 2
Defining the Problem
Why the same scene can produce a sharp photo — or an unusable one
Image quality is the degree to which a captured image faithfully and usefully represents the real scene. It is not a single number — it is the combined outcome of how an image is captured, how much detail it carries, how clean the signal is, and how faithfully geometry is preserved.
The problem this deck investigates:
Given four independent sources of degradation — acquisition conditions, resolution limits, sensor noise, and optical distortion — how does each measurably affect perceived and quantitative image quality, and which is easiest to control?
At a glance
High Quality
Sharp, well-lit,
low noise, true geometry
Degraded
Blurry, noisy,
low-res, warped edges
PROBLEM STATEMENT
02

## Slide 3
Four Factors, One Outcome
The analytical framework used throughout this presentation
Acquisition
Conditions
Lighting, exposure, motion & focus at capture time
01
Resolution
Pixel density and the amount of true detail recorded
02
Noise
Random signal variation that obscures fine detail
03
Distortion
Geometric & optical errors that misplace image content
04
ANALYTICAL FRAMEWORK
03

## Slide 4
01 Acquisition Conditions
What happens in the moment of capture sets the ceiling for everything after
Illumination
Low light forces higher ISO or longer exposure, both of which trade off quality.
Shutter Speed
Too slow relative to motion introduces blur from subject or camera movement.
ISO / Gain
Higher sensitivity amplifies the signal — and the sensor noise with it.
Focus & Distance
Incorrect focus distance or shallow depth of field softens key regions.
The Exposure Triangle
Aperture
Shutter
Speed
ISO
Balanced
Exposure
FACTOR 01 — ACQUISITION
04

## Slide 5
02 Resolution
How many pixels — and how much real detail they actually carry
Spatial resolution is the pixel grid's ability to reproduce fine detail. Beyond raw pixel count, sampling density relative to the scene determines whether detail is genuinely resolved or merely displayed as more pixels (interpolated, not informative).
Low
(e.g. 480p)
Medium
(e.g. 1080p)
High
(e.g. 4K)
More samples per unit area → more genuine detail captured
Chart: Resolution vs. Detail
| 480p (0.3MP) | 720p (0.9MP) | 1080p (2MP) | 4K (8MP) | 8K (33MP)
Perceived Detail Score (0-100) | 28 | 52 | 71 | 90 | 97
Gains diminish past a point — resolution has a real ceiling of usefulness
Key insight: Resolution defines the pixel budget — but noise and distortion decide how much of that budget is usable.
FACTOR 02 — RESOLUTION
05

## Slide 6
03 Noise
Random signal variation that competes with — and can bury — real detail
Shot (Photon) Noise
Inherent randomness in photon arrival; dominant in low light.
Read / Thermal Noise
Electronic noise from sensor readout and heat; constant floor.
Gaussian Noise
Broadband random variation added throughout the imaging chain.
Salt-and-Pepper Noise
Sparse extreme-value pixels from transmission or pixel faults.
Chart: ISO vs. SNR
| ISO 100 | ISO 400 | ISO 800 | ISO 1600 | ISO 3200 | ISO 6400
Signal-to-Noise Ratio (dB) | 42 | 37 | 33 | 27 | 21 | 15
As gain (ISO) rises, amplified noise erodes the usable signal-to-noise ratio
Rule of thumb
A drop of ~6 dB in SNR roughly halves the finest detail level that remains distinguishable from noise — this is why noise reduction and resolution are always evaluated together, not separately.
FACTOR 03 — NOISE
06

## Slide 7
04 Distortion
Geometric and optical errors that misplace or misrepresent content
Undistorted
Grid
Barrel
Distortion
Pincushion
Distortion
Barrel distortion bows lines outward (common in wide-angle lenses); pincushion distortion pulls lines inward (common in telephoto/zoom lenses). Both displace pixels from their true geometric position.
Chromatic Aberration
Lens fails to focus all wavelengths to the same point, causing color fringing at edges.
Perspective Distortion
Apparent size/shape shifts caused by camera angle and subject distance, not the lens itself.
Chart: Distortion Magnitude
| Barrel | Pincushion | Chromatic Aberration | Perspective
Typical Severity (%) | 12 | 8 | 6 | 15
Illustrative values — actual severity depends on lens design and correction software
FACTOR 04 — DISTORTION
07

## Slide 8
Comparative Impact Analysis
Ranking all four factors on impact severity vs. how controllable they are
Chart: Impact vs. Controllability by Factor
| Acquisition Conditions | Resolution | Noise | Distortion
Impact on Perceived Quality | 85 | 60 | 75 | 45
Controllability (post-capture) | 20 | 15 | 55 | 70
Reading the chart
Acquisition conditions have the highest impact but the lowest post-capture controllability — get it right at capture time.
Distortion is highly correctable via lens profiles and software, despite being visually obvious.
Noise sits in the middle: partially fixable, but correction trades off fine detail.
Resolution is fixed at capture; it cannot be meaningfully recovered afterward.
CROSS-FACTOR COMPARISON
08